## Slide 1: Avaya Device Adapter Snap-in - CS 1000 Solution Migration (Modernization) - High Level Architecture
Miloš Pujić
Nov.27, 2017
v.15

## Slide 2: Goals
Facilitate CS 1000 customer retention/conversion to Avaya Aura®

## Slide 3: A “Typical” CS 1000 Customer Solution - Before
Signalling Server Cluster
Primary Data Center
System Management COTS Server
Secondary (Geo-redundant) Data Center
Signalling Server
TPS
PD
Signalling Server
TPS
PD
CS1000 Call Server
UNISTIM
Active
CS
ELAN /
PBX-Link
Signalling Server
TPS
PD
CS1000 Call Server
Hot-Standby
CS
1 Leader
Many Followers
CS1000 Call Server
Hot-Standby
CS
CS1000 Call Server
Active
CS
Active
Hot-Standby
Active
UCM
System Management COTS Server
Standby
UCM
LEGEND
UCM – Unified Communication Manager
CS – Call Server
TPS – Terminal Proxy Server
PD – Personal Directory
CS 1000 MG #1
(aka CS 1000 Shelf with
Line Cards)
TDM
MGC / MG-XPEC
CS 1000 MG#2
(aka CS 1000 Shelf with
Line Cards)
TDM
MGC / MG-XPEC
ELAN – Management LAN
MG – Media Gateway
MGC – Media Gateway Controller
MG-EXPEC – Another type of Media Gateway Controller

## Slide 4: A “Typical” CS 1000 Customer Solution - After
Secondary Data Center
Primary Data Center
UNISTIM over DTLS
PBX-Link
over IPsec
Geo-Redundant
CM
SIP over TLS
SM
Primary Breeze Cluster
ADA
ADA
SM
Primary
Secondary
Active
SMGR
Secondary Breeze Cluster
ADA
ADA
Device Adapter
Primary
CS 1000 MG #1
(aka CS 1000 Shelf with
Line Cards)
TDM
MGC / MG-XPEC
CS 1000 MG #2
(aka CS 1000 Shelf with
Line Cards)
TDM
MGC / MG-XPEC
Standby
SMGR
Device
Adapter
In view of CM, an CS 1000 endpoint is an AST SIP endpoint (analogous to 96X1 SIP)
PBX-Link over IPsec
Existing CS 1000 SW Modules
Legend:
Existing Avaya SW Modules
New SW Module - ADA

## Slide 5: Assumptions
CS1000 Call Server SW is removed from the solution – its functions are now assumed by the ADA snap-in and the Avaya Aura® core (CM, SM)
CS1000 Signalling Server SW components are removed from the solution – the related functions (Terminal Proxy Server – TPS and Personal Directory – PD) are fully assumed by the ADA snap-in
The device adaptation (from CS 1000 Stimulus to SIP AST) is implemented on the Avaya Breeze platform by the Avaya Device Adapter (ADA) Snap-in
  Leverages the Breeze platform
  Leverages the Native C++ Client SDK
Administration of CS 1000 endpoints is done in SMGR
  As in case of other Avaya Aura® SIP endpoint:
    an SM profile is required, as well as
    a CM profile
  In addition, CM supports new endpoint types for CS 1000 endpoints
MGCs in the solutions will likely require firmware upgrade prior to switching them to ADA - This must be done without requiring the CS1000 CS upgrade
  The design team will determine whether to base the implementation on
    Option 1: The new custom MGC firmware (requires upgrade of all MGCs) or
    Option 2: The latest CS 1000 (7.6) MGC firmware (requires upgrade of non-current MGCs)

## Slide 6: Signalling Security
Breeze Cluster
Breeze Server
ADA
Breeze Server
ADA
Breeze Server
ADA
Enterprise Network
Management VLAN
SMGR
SM
TLS[SIP]
MGC
IPsec[PBX-Link+]
MGC
Mgmt
IF
Sec. Mod. IF
Management
Network
GW
Enterprise
Network
GW
ADA provides secure signalling in the following manner:
  SIP & HTTP signalling (towards SM) is protected by TLS
  UNISTIM signalling (towards UNISTIM endpoints) is protected by DTLS
  TDM-set signalling (PBX-Link… - towards MGC) is protected by IPsec in the transport mode
Breeze platform provides support for TLS, but (as of Breeze 3.3) does not support DTLS and IPsec
ADA implementation has to provide support for IPsec and DTLS
In addition, customers may optionally deploy SBCs and VPN GW boxes to additionally streamline and control flow of signalling
  Typical SBC implementation to expect is the Avaya SBC for Enterprise (ASBCE)
  We should expect usage of many brands of VPN GWs, including Avaya ASR-2330 and VSU-10000
DTLS[UNISTIM]
PBX-Link+
Breeze DC
IPsec
DTLS
IPsec
DTLS
TLS
TLS
SIP
HTTP v
UNISTIM

## Slide 7: Avaya Aura® and ADA on Premises
Mgmt VLAN
CM
TDM
Extension
5001
TDM
SIP
CM Administration:
5001: SIP Line
5002: SIP Line
Customer Premises
UNISTIM
Extension
5002
Breeze Cluster
ADA
TCP:
ACP
X11-SSD
New HW Component
Existing HW Component
PBX-Link over IPsec
SM
SIP over TLS
CS 1000 MG
(aka CS 1000 Shelf with
Line Cards)
MGC / MG-XPEC
SMGR
UNISTIM over DTLS
IPsec
IPsec
DTLS
DTLS
TLS
TLS

## Slide 8: Avaya Aura® in Cloud – ADA on Premises Same Breeze Software – Different Deployment
CM
TDM
Extension
5001
TDM
SIP
CM Administration:
5001: SIP Line
5002: SIP Line
Customer Premises
UNISTIM
Extension
5002
Breeze Cluster
ADA
TCP:
ACP
X11-SSD
New HW Component
Existing HW Component
PBX-Link over IPsec
SM
ASBCE
SIP over TLS
CS 1000 MG
(aka CS 1000 Shelf with
Line Cards)
MGC / MG-XPEC
SMGR
Cloud
VPN GW
Customer VPN GW
UNISTIM over DTLS
IPsec
Avaya Aura® 7.1 Cloud VPN solution is reused here for management operations
IPsec
DTLS
DTLS
TLS
TLS

## Slide 9: Avaya Aura® and ADA in Cloud Same Breeze Software – Different Deployment
CM
TDM
Extension
5001
TDM
CM Administration:
5001: SIP Line
5002: SIP Line
Customer Premises
UNISTIM
Extension
5002
Breeze
Cluster
ADA
TCP:
ACP
X11-SSD
New HW Component
Existing HW Component
PBX-Link over IPsec
SIP over TLS
Cloud VPN GW
SM
CS 1000 MG
(aka CS 1000 Shelf with
Line Cards)
MGC / MG-XPEC
SMGR
UNISTIM over DTLS
Customer VPN GW
Avaya Aura® 7.1 Cloud VPN solution is reused here for PBX-Link and UNISTIM signalling
IPsec
IPsec
DTLS
DTLS
TLS
TLS

## Slide 10: Breeze Dependencies
ADA is based on Avaya Breeze™ 3.5 or newer

## Slide 11: CM Dependencies
ADA depends on some CM enhancements slated for Avaya Aura® 8.0
  CS1000-style MADN Support on CM
    Includes both, Single Call Arrangement (SCA) and Multiple Call Arrangement (MCA)
    Supports but does not require new behaviors on the AST SIP endpoints
    An AST SIP endpoint handles both scenarios as the regular CM-style bridging (the bridged-appearance button)
  CM Station Administration Changes in support of CS 1000 endpoints
    New station types for CS 1000 endpoints
      All CS 1000 station types are consider to be SIP stations
    New station fields/attributes for CS 1000 station types:
      CS 1000 Station Type (~ dozen types)
      CS 1000 Terminal Number in terms of : Loop / Shelf / Card / Unit
      Max number of buttons per add-on module page
      Endpoint Features (CLS)
    New button types for CS 1000 station types:
      Conference button
      Transfer button
  CM Call Processing Changes in support of CS 1000 endpoints
    Conference button handling
    Transfer button handling

## Slide 12: SM Dependencies
No SM dependencies have been identified so far
Here is a list of important existing SM “features” that ADA depends on and must fit into
  SM Forgoing SIP Endpoint Authentication
    SM does not challenge SIP requests coming from a trusted SIP entity accessing SM via end-end TLS
    ADA is such an endpoint
  SM Location-based Routing based on the “signalling location”
    ADA indicates the “signalling location” of the caller by the IP address in the “bottom-most Via-header of the INVITE request” (locations must be administered using IP address patterns)
  SM CAC (Bandwidth Management)
    ADA indicates the “media location” of the caller by the IP address in the SDP (locations must be administered using IP address patterns)
PPM Dependencies
Handling of “conference” & “transfer” buttons
  PPM maps these buttons into a “call-appearance” button with the appropriate lable

## Slide 13: ADA Implementation
ADA implements AST SIP endpoint emulation for every CS 1000 endpoint it serves (UNISTIM and TDM endpoints)
Supported CS 1000 endpoints are ‘thin’ aka ‘stimulus’ endpoints
  The stimuli include:
    Endpoint  Controller direction: Hook status, Keypad presses, Key/button presses, Endpoint registration (IP endpoints) …
    Controller  Endpoint direction: Ringer control, Key/button-lamp control, Display control, Media commands (IP endpoints) …
  ADA and endpoints exchange the stimuli over the ‘PBX link’
    IP endpoints: ‘PBX Link’ is established between ADA and a TPS
    TDM endpoints: ‘PBX Link’ is established between ADA and a TPS
  ADA exchanges AST SIP signaling with SM/CM
An ADA instance serves a group of CS 1000 endpoints
  An ADA instance emulates a bunch of AST SIP endpoints – one for each ‘real’ CS 1000 endpoint
  An ADA instance handles stimuli for a number of ‘real’ CS 1000 endpoints
  For each CS 1000 endpoint, ADA runs an ‘endpoint state-machine’ logic that is driven by SIP interactions with SM/CM one side and stimulus interactions with real endpoints on the other side
The idea here is to use a Client SDK as the basis for the AST SIP endpoint emulation

## Slide 14: ADA Implementation
          Breeze Server
C++ CSDK
[Linux Process]
Use the Native C++ CSDK in Multi-user Mode
  Main functionality is implemented outside WAS (as a number of Linux processes)
  We still need an ADA snapin
  The ADA snapin instantiates the master Linux process that acts as a group controller / proxy for a number of CS 1000 endpoints
  The ADA snapin provides access to the Avaya Aura® System Management data
  The ADA snapin instantiates the Group Controller / Endpoint Proxy and provides configuration for every dependent CS 1000 endpoint
  A SIP endpoint emulation is supported by a single native C++ CSDK instance for all CS 1000 endpoints (multi-user mode of the CSDK)
    Each endpoint emulation gets a configuration file at instantiation time and has to be ready to receive configuration updates during run time (no PPM usage)
  The group controller acts as proxy for accessing endpoints’ media engines and I/O operations (via PBX Link)
ADA Snap-in
[WAS]
Group Controller / Endpoint Proxy
[Linux Process]
Endpoint Emulator #1
[Object]
Endpoint Emulator #n
[Object]
…
Instantiates
Provides Config
MGC
SM
PBX-Link
SIP
SMGR
Needs to support several thousands of endpoints!
Need proof of concept
One TLS socket per endpoint! Scalability?
Supports rich telephony!
UNISTIM

## Slide 15: ADA Implementation – TPS & PD Elimination
Leaving the TPS in the customer solutions going forward has significant repercussions from both, customer perspective and R&D delivery effort perspective:
  Customer aspect
    Extra servers in the solution
    Increased power consumption
    Extra IP address assignment
    Extra security considerations
    Patching of the TPS software
    …
  R&D Delivery aspect
    “Bringing up” the TPS in the environment without CS 1000 CS
    IPSec support (IPSec not supported by Breeze, ADA take full ownership)
    JITC accreditation with IPSec has significantly increased scope
    …
The above has driven the decision to eliminate the original TPS from the solution

## Slide 16: ADA Implementation
          Breeze Server
Native C++ CSDK in Multi-user Mode with “Internal” TPS
ADA Snap-in
[WAS]
SMGR
Instantiates
Provides Config
ADA Linux process(es)
RUDP
USI LIB
VTM
Reverse DSET
SSD LIB
CS 1000 Endpoint App.
RUDP
USI LIB
ELC
RUDP
USI LIB
CSV
VTI LIB
PBX LIB Server
WAP
PD (optional)
HTTPS
UNISTIM
MGC
PBX-Link
UNISTIM
C++ CSDK
[Linux Process]
Endpoint Emulator #1
[Object]
Endpoint Emulator #n
[Object]
SM
SIP
TDM - UNISTIM Adaptation
Card LAN
X

## Slide 17: ADA integration with the SM Origination-based Routing
How to extend SM differentiated routing to the non-SIP devices situated in different physical locations (i.e., allow non-SIP devices behind the Avaya Device Adapter (ADA) enjoy the current location-based routing)?
ADA adhering to the following would achieve the purpose without any SM changes:
  When registering on behalf of a non-SIP endpoint, the ADA includes an extra Via header containing an IP address that belongs to the IP address map of the device’s location. The Contact header will continue to point to ADA’s address.
  When initiating a call on behalf of a non-SIP endpoint, the ADA includes an extra Via header containing an IP address that belongs to the IP address map of the device’s location. The Contact header will continue to point to ADA’s address.
  When processing the Register and Invite responses, which follow the Via header contents, ADA consumes the message (and not try to forward the message to the next hop).
Rather than establishing the location using the Contact header (which will incorrectly make each endpoint appear to be at the same location as that of the ADA), SM will establish the location of the endpoint using the bottom most Via header. This approach is similar to the bottom-most Via header based location determination (hence routing) provided to the non-SIP CM endpoints. With the original bottom-most Via header approach, CM doesn’t register with SM; whereas, with the ADA approach, ADA will register on behalf of the non-SIP endpoint.

## Slide 18: Avaya Aura® in AWS – VPN Solution
Aura in AWS is using an on premises VPN Gateway (aka VPN Service Unit - VSU) to connect to the Virtual Private Gateway of the AWS Virtual Private Cloud (VPC)
  AWS Virtual Private Gateway and on premises VPN Gateway need to be administered for IPSec in a compatible fashion
  Once the routing and firewalls are setup the gateways can connect via a secure connection
Most IPSec VPN Gateway implementations should be able to connect to the AWS VPC Virtual Private Gateway
  Was Avaya Secure Router ASR-2330 tested?
  Was Avaya VPN Service Unit VSU-xxxx tested?
An alternative to using AWS VPC Virtual Private Gateway is to deploy a softVPN in AWS
A reference VPN connectivity to AWS VPC:

## Slide 19: Internal TPS Implementation Notes
Leader election implementation can be eliminated – use Breeze “Cluster IP” as the “Node IP”
  The Breeze server that “hosts” the “Cluster IP” is the Leader; other servers from the cluster are the Followers
  ADA needs an API to get the “Cluster IP”
  ADA needs an eventing API to know whether the server is the “owner” of the “Cluster IP” – to be verified whether such an API exist
UNISTIM endpoint Load balancing (CSV) needs to be implemented
  CSV runs on the Leader
  The Followers need to share the information with the Leader about their current load (in terms of the number of UNISTIM clients they support at any point in time)
    The existing broadcasting-based TPS status sharing can be eliminated
    Instead, use data-grid to share the information
TPS ELC service can be eliminated
  There is no value that ELC adds
  CSV should redirect an UNISTIM endpoint directly to the working TPS
TPS communicates with the external PD over HTTPs
  This is in support for the Directory, Caller and Redial lists on UNISTIM endpoints
  HTTP requests are originated by TPS i.e. TPS acts as an HTTP client and PD as the HTTP server

## Slide 20: MGC Support Notes
Use a VPN GW to secure MGC  ADA communication
MGC  ADA Communication includes:
    PBX-Link (TCP port 15000 on ADA)
    Card/Unit related signalling (TCP port 32781)
    RPC connection (TCP port32788)
    Heartbeat (UDP port 32779 on ADA)
    Any other?
  Notes:
    On MGC, card LAN and SSD phone messages are carried in SSD TCP connection on port 32781.
    There must be a heartbeat UDP connection on port 32779.
    MGC also performs a registration request to call server via RPC on port 32788 during startup.
    These are mandatory connections.

## Slide 21: MGC Support Notes…continued
Digital Line Card / Digital Set Status
  Status of a digital set will drive SIP registrations/unregistrations
  When MGC starts up it resets all IPE cards. This is the same when card is inserted.
  Once DLC card is detected, a CLAN XMI002 message is sent to CS. Also, all unit memory blocks on that card is marked for audit.
  There’s a special polling audit running on MGC to poll all slots on DLC card if it’s enabled.
  Audit picks up those blocks and starts polling a31 chip.
  If there’s a phone connected, the phone (or fpga) responds.
  Audit gets the response and sends SSD message 0x0709 – unit is equipped – towards call server.
  Call server handles it and starts regular phone initialization.
  Audit keeps polling all slots including the phone that just found.
  The phone gets unplugged.
  Audit receives no responses in say 0.5 sec, declares it as not equipped and sends SSD 0x070A towards CS. CS marks unit as not present.
  When card is ejected, clan sends XMI001. Have not checked if units on CS are put to disabled state upon xmi001 or set-not-found SSD… but should be either reason.

## Slide 22: Background Information: CS 1000 Protocol Stack
TPS
How much of the TPS should we keep in the ADA architecture?
  Whole TPS?
  Just bottom 2 layers?
RUDP
USI LIB
VTI LIB
DSET
SSD LIB
Call Processing
Application
RUDP
USI LIB
ELC
RUDP
USI LIB
CSV
UNISTIM
Extension
5001
Port: 7300
Port: 5100
Port: 4100
1
2
3
TCP:
RAS
ACP
X11-SSD
UDP:
- UNISTIM
CS 1000 MG
MGC
TDM
Extension
5002
Integration Point #1
VTM
PBX LIB
Integration Point #2
Integration Point #3
Port: 15000
WAP
Choice of integration points (not limited to):
TCP:
ACP
X11-SSD
PD

## Slide 23
11xx Series
  GEM (Graphic Expansion Module)
  Has 18 keys
  Not all models support the GEM e.g. 1110 does not, but 1120E/1140E/1150E/1165E do
  Up to 3 GEMs per set
  Note:
    The sets and GEM are still supported
    Only 1120E and 1140E are still in production (and we just did the LTB for their CPU)
i20xx
  i2002 & i2004 support 24-key LCD KEM
    With Shift provides 48 keys
    Up to 2 KEMs per set
12xx Series
  Has two KEMs models: 18-key LED KEM and 12-key LCD KEM
  Not supported on 1210, but supported on 1220 and 1230 (I believe this is a CS1k marketing limitation)
  Up to 3 LED KEMs per set (? - BCM only support up to 2 so CS1k may have the same limitation)
  Up to 7 LCD KEMs per set
  Note:
    The sets and KEMs are still supported
    All three set models are still in production (but we have already did the LTB for their CPU a while back)
    LED KEM has not been production for many years
M39xx Series
  Has two expansion modules: 22-key KBA (Key Based Accessory) and 8-key DBA (Display Based Accessory)
  Up to 2 KBAs and 3 DBAs per set are supported on the M3904 and M3905(ph3)
  Note:
    The sets and KBA are still supported
    DBA was EoS in 2012
    The last product in the M3900 family that is still in production is the 3904 and that will end this year (as soon as next quarter)
Aries
  22-key AOM
  Up to 2 AOMs per set
CS 1000 Expansion Modules

## Slide 24
CS 1000 Expansion Modules
39xx 8-key DBA
39xx 22-key KBA
11xx with 18-key GEM (KEM3)
i20xx with 24-key LCD KEM
(2xKEM4)
12xx 18-key LED KEM (KEM3)
12xx 12-key LCD KEM (KEM4)
Aries with 22-key AOM

## Slide 25: Add-on Module Support by ADA
Several add-on module types are supported on CS1000
  11XX endpoints (IP) GEM (Graphic Expansion Module)
    18 physical keys (possibility of 2 pages with SHIFT); max 3 modules
  12XX series endpoints (IP) 12-key LCD KEM
    12 physical keys (possibility of 2 pages with SHIFT); max 3 modules
  12XX series endpoints (IP) 18-key LED KEM
    18 physical keys; max 2 modules; paper labels
  20xx series endpoints (IP) 24-key LCD KEM
    24 physical keys; max 2 modules
  Aries (2216|2616) endpoints (Digital) 22-key AOM (Add-On Module)
    22 physical keys; max 2 modules; paper labels
  39xx series endpoints (Digital) 22-key KBA (Key Based Accessory)
    22 physical keys; max 2 modules
  39xx series endpoints (Digital) 8-key DBA (Display Based Accessory)
    8 physical keys; max 2 modules
CM Endpoint Administration – New Attributes for CS1000 endpoints behind CA
  CS1000 Endpoint Type
  Number of Add-on Module Pages – “Button Module Pages”
  Number of Keys/Buttons per Page – “Buttons per Page”

## Slide 26: Add-on Module Support by ADA…
Add-on Module | CS1000 |  | CM |  | Notes
18-Key GEM for 11xx Series Endpoints | TYPE=1140 CLS KEM3 |  | CS1000-Type=1140 Buttons-per-Page=18 |  | Starting Key Number on 1st module: 32
 | KEM | 1 | Button-Module-Pages | 2 (because of the SHIFT) | Total Keys: 68 (32+2x18)
 | KEM | 2 | Button-Module-Pages | 2 | Total Keys: 68 (32+2x18)
 | KEM | 3 | Button-Module-Pages | 3 | Total Keys: 86 (32+3x18)
12-Key LCD KEM for 12xx Series Endpoints | TYPE=1230 CLS KEM4 |  | CS1000-Type=1230 Buttons-per-Page=12 |  | Starting Key Number on 1st module: 32
 | KEM | 1 | Button-Module-Pages | 2 (because of the SHIFT) | Total Keys: 56 (32+2x12)
 | KEM | 2 | Button-Module-Pages | 3 (because of the 2x SHIFT) - 4th page not supported | Total Keys: 68 (32+3x12)
 | KEM | 3 | Button-Module-Pages | 3 | Total Keys: 68 (32+3x12)
 | KEM | 4 | Button-Module-Pages | - not supported | ---
18-Key LED KEM for 12xx Series Endpoints | TYPE=1230 CLS KEM3 |  | CS1000-Type=1230 Buttons-per-Page=18 |  | Paper labels. Starting Key Number on 1st module: 32
 | KEM | 1 | Button-Module-Pages | 1 | Total Keys: 50 (32+18)
 | KEM | 2 | Button-Module-Pages | 2 | Total Keys: 68 (32+2x18)
24-Key LCD KEM for 20xx Series Endpoints | TYPE=2004 CLS KEM4 |  | CS1000-Type=2004 Buttons-per-Page=24 |  | Starting Key Number on 1st module: 32
 | KEM | 1 | Button-Module-Pages | 1 | Total Keys: 56 (32+1x24)
 | KEM | 2 | Button-Module-Pages | 2 | Total Keys: 80 (32+2x24)

## Slide 27: Add-on Module Support by ADA…
Add-on Module | CS1000 |  | CM |  | Notes
22-Key AOM for Aries Endpoints | TYPE=2216¦2616 CLS AOM |  | CS1000-Type=2216¦2616 Buttons-per-Page=22 |  | Paper labels. Starting Key Number on 1st module: 16
 | KEM | 1 | Button-Module-Pages | 1 | Total Keys: 38 (16+22)
 | KEM | 2 | Button-Module-Pages | 2 | Total Keys: 60 (16+2x22)
22-Key KBA for 39xx Endpoints | TYPE=3904¦3905 CLS KBA |  | CS1000-Type=3904¦3905 Buttons-per-Page=22 |  | Starting Key Number on 1st module: 32
 | KEM | 1 | Button-Module-Pages | 1 | Total Keys: 54 (32+22)
 | KEM | 2 | Button-Module-Pages | 2 | Total Keys: 76 (32+2x22)
8-Key DBA for 39xx Endpoints | TYPE=3904¦3905 CLS DBA |  | CS1000-Type=3904¦3905 Buttons-per-Page=8 |  | Starting Key Number on 1st module: 32
 | KEM | 1 | Button-Module-Pages | 1 | Total Keys: 40 (32+8)
 | KEM | 2 | Button-Module-Pages | 2 | Total Keys: 48 (32+2x8)

## Slide 28: CM Expansion Modules
  CM supports up to 3 button modules
CM numbers buttons based on certain “sections”:
  Those on the main phone are considered part of the Feature Module.
  Those in Button Modules are all collectively considered part of the Coverage Module.
  Thus, for a phone with 96 buttons, the buttons are numbered Feature Module (Section 1) 1-24 and Coverage Module (Section 2) 1-72.
The numbering that PPM uses when sending buttons to the phone is simpler:
  When PPM sends the button data to the phone, the button index is from 1-96 (verified by traceSM).
  There is no module concept at all when PPM download the data to the phone.

## Slide 29: CM Expansion Modules …
Endpoint button definitions are stored in 3 SMGR tables
  ‘ipt_button’ table
  ‘ipt_feature_button’ table
  ‘ipt_expmodule_button’ table
  ‘label’ column represents the button number